## Slide 1: Semantic Graphs for Modeling Cyber-Physical Systems
Or, how to do work with large amounts of data from complicated systems that are all unique, constantly changing, and have no good documentation
Dr. Gabe Fierro
https://gtf.fyi
Assistant Professor, Computer Science
Joint Appointment @ NREL

## Slide 2: There’s Data Everywhere
Internet of Things:
  Cheaper, more ubiquitous sensors
  Digital control and monitoring systems
  Data-oriented processes, techniques
More data about cyber-physical systems than ever before
This data is difficult to discover, access, and understand
We are data rich, but information poor

## Slide 3: There’s Data Everywhere
Zoom in on buildings:
  75% of US electricity, 40% of energy consumption
  Thousands of sensors, control points
Decades of research into data-driven applications
  Grid-aware operation
  Occupant comfort
  Automated fault detection
  Intelligent controls
  Etc…
PHEVs
Chillers
Servers
Fans
Information & Communications Technology (ICT) Systems
Lighting
Building Automation & Control System
Solar PV
AHUs
Stats
Meter
Cameras
Smart Grid
Battery Storage
SubMeter

## Slide 5: What’s in a Name?
SODA1R465__ARS
SODA1R465__ARS
Site name
SODA1R465__ARS
Air Handling Unit
SODA1R465__ARS
Equip ID
SODA1R465__ARS
Zone/Room
Zone Name
SODA1R465__ARS
Padding / delimiter
SODA1R465__ARS
Zone Air Temperature Setpoint
SODA1R465__ARS
AHU
VAV box
Zone
Thermostat
72F
Setpoint control target
Labels like these often the only up-to-date and readily-available source of metadata
Site-specific conventions; sometimes no labels at all
No consistent, standard metadata for cyberphysical system data

## Slide 8: New Platforms for Data-Driven Cyber-Physical Systems
Investigate new hybrid graph/timeseries data systems for data-driven IoT/CPS applications
Enable new applications of ML/AI in CPS at scale
Developing new techniques for efficient query processing, logical inference over societal-scale graphs linked with telemetry
Standardized, machine-readable metadata for CPS
Novel semantic graph-based representations of topology and composition
  Buildings (Brick: https://brickschema.org/)
  Smart Grids (in progress)
  ASHRAE, DOE, NREL, PNNL, LBNL collaborations
Enable uniform discovery of resources at scale
Have data about real-world systems/environments? Send me an email! gtfierro@mines.edu